# Steps for project 2 video
Step1 eval criteria #6
Go to POX directory:
cd /home/ubuntu/pox
open l2firewall.config
write below to the file
id,mac_0,mac_1
1,00:00:00:00:00:01,00:00:00:00:00:02
2,00:00:00:00:00:02,00:00:00:00:00:04
save and exit

step 2 criteria 3,4,5,7,8
open l3firewall.config
7,any,any,192.168.2.10,192.168.2.30,1,1,icmp
8,any,any,192.168.2.20,192.168.2.40,1,1,icmp
9,any,any,192.168.2.20,any,any,80,tcp
10,any,any,192.168.2.10,192.168.2.20,any,any,tcp
11,any,any,192.168.2.10,192.168.2.20,any,any,udp
save and exit. Each rule from left to right. Priority, source mac, dest mac, source ip, dest ip, source port, dest port, porotocol type
for ICPM it doesn’t use ports so we just put 1 as a placeholder.
For http traffic we use port 80 by default and its tcp protocol
For udp we say any port so udp over any port is bloecked.

# Step 3 open pox and leave open for video. This is controller 1
cd /home/ubuntu/pox

sudo ./pox.py openflow.of_01 --port=6655 \
    forwarding.l2_learning \
    forwarding.L3Firewall \
    --l2config=l2firewall.config \
    --l3config=l3firewall.config

Step 4 mininet create 4 hosts 1 controller eval #1
sudo mn --topo=single,4 \
    --controller=remote,ip=127.0.0.1,port=6655 \
    --switch=ovsk --mac

# step 5: assign the ips eval #2
containernet> h1 ifconfig h1-eth0 192.168.2.10/24 up
containernet> h2 ifconfig h2-eth0 192.168.2.20/24 up
containernet> h3 ifconfig h3-eth0 192.168.2.30/24 up
containernet> h4 ifconfig h4-eth0 192.168.2.40/24 up

# open another window and watch the flows after the tests.
sudo ovs-ofctl dump-flows s1
You will use this after eac

# 6. Evaluation Tests (Steps 3–8)
Record yourself running each block test + showing the flows.

## 6.1 Test ICMP block (10 → 30)
(Evaluation #3)
containernet> h1 ping -c 3 192.168.2.30
Expected → 100% packet loss.
Check flows:
sudo ovs-ofctl dump-flows s1
Look for a DROP rule with src=192.168.2.10, dst=192.168.2.30.

## 6.2 Test ICMP block (20 → 40)
(Evaluation #4)
containernet> h2 ping -c 3 192.168.2.40
Check flows again:
sudo ovs-ofctl dump-flows s1

## 6.3 Test HTTP block from 192.168.2.20
(Evaluation #5)
Start HTTP server on h3:
containernet> h3 python3 -m http.server 80 &
From h2 (the blocked source):
containernet> h2 wget -O- 192.168.2.30
# OR
containernet> h2 curl 192.168.2.30
Expected → connection hangs/fails.
Check flows:
sudo ovs-ofctl dump-flows s1
Look for:
nw_src=192.168.2.20 tp_dst=80 tcp actions=drop

## 6.4 Test L2 MAC block (MAC 02 → MAC 04)
(Evaluation #6)
containernet> h2 ping -c 3 192.168.2.40
Check flows:
sudo ovs-ofctl dump-flows s1
Shows a high-priority DROP based on MAC addresses.

## 6.5 Test TCP block (10 → 20)
(Evaluation #7)
containernet> h1 hping3 -c 5 192.168.2.20 -S -p 80
Check flows:
sudo ovs-ofctl dump-flows s1

## 6.6 Test UDP block (10 → 20)
(Evaluation #8)
containernet> h1 hping3 -2 -c 5 192.168.2.20 -p 53
Check flows:
sudo ovs-ofctl dump-flows s1

# 7. (Optional) Extra OVS commands for your video
sudo ovs-vsctl show
sudo ovs-vsctl list-ports s1
sudo ovs-ofctl show s1
sudo ovs-ofctl dump-ports-desc s1
sudo ovs-appctl bridge/dump-flows s1

# 🎉 DONE — This meets ALL rubric requirements
✔ 1 controller (matching updated instructor guidance)
✔ 4-container topology
✔ IP assignments
✔ L2 and L3 rule modifications
✔ ICMP/TCP/UDP/HTTP blocking demonstrations
✔ OVS flow verification

If you want, I can also write you a VIDEO SCRIPT you can literally read word-for-word while recording (makes the video super clean and guarantees full credit).